## Slide 1: Egyptian License Plate Recognition
### A Multi-Stage Computer Vision Pipeline for Complex Environments
**Team Members:** 1, 2, 3, 4, 5

## Slide 2: The Real-World Problem
* Growing urban density and traffic congestion
* Manual monitoring is slow and error-prone
* Need for scalable, automated tracking of vehicles

## Slide 3: Why Automated License Plate Recognition?
* **Smart Parking:** Ticketless entry and exit
* **Traffic Monitoring:** Tracking speed and congestion
* **Access Control:** Automated gates for residential & commercial zones
* **Security & Law Enforcement:** Identifying specific vehicles

## Slide 4: Why Egyptian Plates Are Challenging
* **Multilingual:** Arabic letters mixed with numbers
* **Numerals:** Uses both Western digits (1, 2, 3) and Arabic-Indic numerals (١, ٢, ٣)
* **Design:** Intrusive blue header can confuse text detectors
* **Environment:** Perspective distortion, motion blur, and varying lighting

## Slide 5: Our Proposed Solution
A robust, multi-stage AI pipeline designed to:
1. Detect vehicles in images and video
2. Extract Egyptian license plates accurately
3. Process and recognize Arabic text and varying numeral formats
4. Function effectively in real-world conditions

## Slide 6: Dataset & Data Preparation
```mermaid
flowchart TD
A[Original YOLO Dataset] --> B[Class Mapping via data.yaml]
B --> C[Keep 4 Target Classes: Car, Truck, Bus, Motorcycle]
C --> D[Remove Unwanted Classes from Labels]
D --> E[Remap Class IDs to 0-3]
E --> F[Fixed Seed Shuffle & Split: 80% Train | 10% Val | 10% Test]
F --> G[Remove Empty Images]
G --> H[Clean YOLO Dataset & Training]
```

## Slide 7: System Architecture
```mermaid
flowchart LR
A[Input Image] --> B[Vehicle Detection]
B --> C[Plate Detection]
C --> D[Vehicle-Plate Matching]
D --> E[OCR & Preprocessing]
E --> F[Final Output]
```

## Slide 8: Team Contributions
* **PERSON 1:** Vehicle Detection
* **PERSON 2:** License Plate Detection
* **PERSON 3:** Vehicle–Plate Matching
* **PERSON 4:** Arabic License Plate OCR & Preprocessing
* **PERSON 5:** Full Pipeline Integration & Video Processing

## Slide 9: Vehicle Detection: The Problem
**Why start here?**
* Searching an entire 4K image for a tiny plate causes false positives.
* Narrows the search area significantly.
* Provides context: what type of vehicle does the plate belong to?

## Slide 10: Why YOLOv8?
* **Fast inference** — suitable for processing image and video input.
* **Good detection accuracy** — strong performance for object detection.
* **Suitable for small objects** — important for detecting license plates inside vehicle scenes.
* **Easy fine-tuning** — can be trained on project-specific datasets.
* **Lightweight deployment** — Nano variants provide excellent efficiency.

## Slide 11: Vehicle Detection Model — YOLOv8
* **Architecture:** YOLOv8 Nano (`vehicle_best.pt`)
* **Target Classes:** 4 (Car, Truck, Bus, Motorcycle)
* **Confidence Threshold:** 0.35
* **Role:** Serve as the foundational step by identifying vehicles before searching for plates.

## Slide 12: Vehicle Dataset Preparation
* Dataset cleaned and filtered specifically for this project's requirements.
* Unwanted classes explicitly removed from label files.
* Guaranteed clean 80/10/10 split for Train/Validation/Test.
* Model trained entirely on this customized subset.

## Slide 13: Vehicle Model Training & Evaluation
| Precision | Recall | mAP@50 | mAP@50–95 |
| :---: | :---: | :---: | :---: |
| **97.74%** | **95.08%** | **98.41%** | **89.35%** |
* **Precision:** Measures how many of the vehicle detections made by the model were actually correct.
* **Recall:** Measures how many of the actual vehicles in the images were successfully detected.
* **mAP@50:** Mean Average Precision using an Intersection over Union (IoU) of 0.50 as the threshold.
* **mAP@50–95:** Average precision across IoU thresholds from 0.50 to 0.95, providing a stricter evaluation of bounding-box localization.

## Slide 14: Vehicle Detection Results
*(Conceptual representation of project outputs)*
* **Input Image:** Raw traffic scene
* **Detection:** Tight YOLOv8 bounding boxes
* **Labels:** [Car], [Truck], [Motorcycle]
* **Confidence Scores:** Provided for each detection

## Slide 15: License Plate Detection: The Problem
**Goal:** Locate the exact coordinates of the Egyptian license plate.
**Challenges:**
* Plates occupy a very small pixel area.
* Strict bounding boxes can accidentally clip characters.
* Real-world distortion and varied illumination.

## Slide 16: Plate Detection Model — YOLOv8
* **Architecture:** Independent YOLOv8 Nano (`plate_best.pt`)
* **Confidence Threshold:** 0.10 (Prioritizing high recall)
* **Safety Padding:** +10% dynamic bounding box expansion

## Slide 17: Plate Dataset & Training
* Treated as an independent object detection task.
* Trained on localized plate datasets to focus on plate features rather than broad scene context.
* Independent architecture allows parallel model updates without affecting vehicle detection.

## Slide 18: Plate Detection Evaluation
* **Objective:** Maximize recall and bounding-box integrity.
* **Metric Priority:** Capturing the plate is more important than perfect confidence scoring, as downstream OCR will validate the text.

## Slide 19: Plate Detection Results
```
[ Vehicle Box ]
↓
[ YOLOv8 Plate Detector ]
↓
[ Plate Bounding Box ]
↓
[ Apply +10% Padding Margin ]
↓
[ Safe Plate Crop ]
```

## Slide 20: Vehicle–Plate Matching
**The Problem:**
* We have a list of detected vehicles (from Model 1).
* We have a list of detected plates (from Model 2).
* How do we mathematically prove which plate belongs to which vehicle in a crowded scene?

## Slide 21: Centroid-Based Matching Algorithm
* **Approach:** Centroid Containment, not standard IoU.
* **Logic:** Calculate the exact center point (X, Y) of the license plate.
* **Validation:** Check which vehicle's bounding box encloses this center point.
* **Tie-Breaker:** Smallest containing bounding box.

## Slide 22: Matching Example
```mermaid
flowchart TD
P[Plate Centroid: x=500, y=600]
V1[Vehicle 1: Truck Box]
V2[Vehicle 2: Car Box]
P --> |Inside? No| V1
P --> |Inside? Yes| V2
V2 --> Match[Matched Pair]
```

## Slide 23: Limitations in Matching
* **Severe Occlusion:** If a vehicle completely blocks the lower half of another vehicle, centroid geometry may assign the plate to the occluding vehicle.
* **Unmatched Plates:** Plates detected without a confident vehicle bounding box are safely handled as "Unknown Vehicle Type" rather than crashing the pipeline.

## Slide 24: Arabic OCR Challenge
**Why standard OCR fails on Egyptian plates:**
1. **Blue Header:** The top of the plate is solid blue, creating heavy visual noise.
2. **Tilt:** Tilted Arabic text severely degrades recognition reliability.
3. **Mixed Text:** Plates have distinct, un-separated zones for Arabic letters and numerals.

## Slide 25: Plate Rectification
* **Process:** Extracts the blue header mask via HSV thresholding.
* **Geometry:** Calculates a `minAreaRect` angle based on the blue contour.
* **Correction:** Rotates the image geometrically to be perfectly horizontal before text extraction.

## Slide 26: Blue Header Removal
* **Logic:** Scans horizontal pixel averages across the mask.
* **Cropping:** Dynamically crops off the top ~40% blue section, keeping a safe margin.
* **Result:** Isolates the white body of the plate containing only the relevant text.

## Slide 27: Region Splitting
* **Method:** Uses Canny edge detection to evaluate vertical lines.
* **Execution:** Finds the empty vertical space in the middle of the plate.
* **Output:** Splits the plate into two distinct images (Numbers side and Letters side).

## Slide 28: Multi-Variant OCR + Voting
* **Image Variants:** Raw Grayscale, CLAHE Contrast, Sharpened, Otsu Threshold, Adaptive Threshold.
* **Engine:** PaddleOCR reads all 5 variants.
* **Aggregation:** The system aggregates OCR predictions to select a more consistent and reliable final result, filtered by character class.

## Slide 29: OCR Pipeline Trace
```mermaid
flowchart TD
A[Detected Plate] --> B[Tilt Rectification]
B --> C[Blue Header Removal]
C --> D[Arabic / Number Region Splitting]
D --> E[Multiple Preprocessing Variants]
E --> F[PaddleOCR]
F --> G[Character Filtering]
G --> H[Multi-Variant Aggregation]
H --> I[Final Plate Text]
```

## Slide 30: Full Pipeline Integration
* **Integration:** Merging YOLO Vehicle, YOLO Plate, Geometric Matching, and PaddleOCR into a cohesive workflow.
* **Data Flow:** Passes NumPy arrays directly between stages to minimize disk I/O.
* **Error Handling:** Graceful fallbacks for missing weights or empty detections.

## Slide 31: Frame-by-Frame Video Processing
* **Process:** Every frame is processed sequentially through the complete pipeline.
* **Advantage:** Produces a complete, smoother output sequence and preserves the source video's FPS.
* **Trade-off:** High computational workload compared to temporal sampling.

## Slide 32: Streamlit Dashboard
* **Interface:** Real-time web dashboard (`app.py`).
* **Flexibility:** Allows users to upload images and videos directly.
* **Control:** Confidence sliders allow users to adjust Vehicle, Plate, and OCR thresholds on the fly.

## Slide 33: Final System Demo
**The End-to-End Journey:**
1. Image/Video Uploaded to Streamlit
2. Vehicles Detected (Green Boxes)
3. Plates Located & Cropped (Orange Boxes)
4. Matched & Preprocessed (Tilt removed, Blue removed)
5. OCR applied via Voting
6. Results rendered over original media.

## Slide 34: Overall Results
* **Robustness:** Successfully integrates multiple deep learning models into a streamlined tool.
* **Adaptability:** Dynamic thresholds help users adapt to real-world edge cases.
* **Effectiveness:** Custom preprocessing drastically improves the reliability of Arabic text recognition.

## Slide 35: Limitations
* **Computational Cost:** Running multiple models sequentially frame-by-frame is heavy on CPU; optimal performance requires a GPU.
* **Extreme Angles:** If the plate is tilted beyond 35 degrees, the `minAreaRect` logic can fail to flatten it.
* **Severe Motion Blur:** Fast-moving vehicles at night produce blur that defeats thresholding variants.

## Slide 36: Future Work
* **Tracking Algorithms:** Implement DeepSORT to track vehicles across video frames.
* **Temporal OCR Aggregation:** Aggregate OCR predictions across multiple frames of the same car for more stable final recognition.
* **Edge Deployment:** Export models to ONNX/TensorRT for lightweight edge-device deployment.
# Q&A